## Slide 1
2023. 6. 14
Handong Global University
School of Mechanical and Control Engineering
Robot Control System
for Motion Tracking and Precise Parsing in Disaster Sites
2023-1 Industrial AI and Automation
Advisor: Prof. Young-Keun Kim
Seok-Won Jung
Tae-Woong Song
Jin-Ho Kook
Jae-Hyun Oh
21400000
21700394
21800031
21900000
Notes: 재난 현장 내 잔해 ㅈ모션 트래킹 정말 파징 시스템

## Slide 2
▣ Demo Video
Motion Tracking / Precise Parsing Demo Video

## Slide 3
▣ Introduction
1
2
3
4
Typhoons, earthquakes, radioactivity, building collapse, etc
Obstacle elimination
Life loss during recovery
(building collapse / overwork)
Radiation exposure
Damage situation identification
Analysis / reporting of disaster response status
Accident cause investigation
Continuous management of disaster sites
Disaster Occurrence
Retrieval & Recovery
Initial Response
Disaster Relief
Notes: 재난 복구 작업 순서
재난 발생
손상 상황 식별 재해 대응 현황 분석 및 보고
인명 피해 없는 장애물 처리
재난 원인 조사 및 재해지역 지원

## Slide 4
▣ Introduction
Project Goal
1) Vision sensor- based motion tracking control
Relative angle error within 10
2) Vision sensor-based robot end-effector angle control
○ Robot system for motion tracking and precise parsing
Debris removal system using a robot is required
Problems
Goal

## Slide 5
▣ Research Contents
Algorithm Flow
Robot system for motion tracking and precise parsing
1-1) Image Processing for Motion Tracking
1-2) Image Processing for Catching Debris
3) Robot Control
- Mode 1 for Moving to Debris
- Mode 2 for Cleaning Debris
2) Data Acquisition
From Arduino
/
/
Parameter | Unit | Description
 |  | x-coordinate in the robot absolute coordinate system
 |  | y-coordinate in the robot absolute coordinate system
 |  | Robot end effector angle
 |  | Debris recognition status
 |  | Distance to debris
Parameter | Unit | Description
 |  | x-coordinate in the robot absolute coordinate system
 |  | y-coordinate in the robot absolute coordinate system
 |  | Robot end effector angle
 |  | Debris recognition status
 |  | Distance to debris

## Slide 6
▣ Research Contents
Color segmentation for object tracking
Pixel to robot absolute coordinate
Sending / to robot control part
Color segmentation for detecting debris
Get using geometry approximation algorithm
Coordinate conversion ( )
Sending to robot control part
○ Image Processing Part
1-1) For Motion Tracking
1-2) For Catching Debris
Robot system for motion tracking and precise parsing
Coordinate Transformation
Angle Detection
Notes: 높이 측정 알고리즘을 간략하게 설명드리면,
k-means 거리 기반 클러스터링으로 각 벽돌의 데이터를 분리하였습니다.
이후 거리정보를 의미하는 z-축 데이터에 이동 평균 필터를 사용해서 노이즈를 감쇄하였습니다.
마지막으로 rms 값을 추출하여 물체의 높이를 추정하였습니다.

## Slide 7
▣ Research Contents
Connection distance sensor with Arduino
Serial communication between robot and Arduino
Mode 1
Receiving / / from image processing part
/ input to robot / Change Mode 2
Mode 2
Receiving from image processing part (1-2)
Receiving from Arduino
/ input to robot
○ Arduino / Robot Control Part
2) Data Acquisition from Arduino
3) Robot Control
Robot system for motion tracking and precise parsing
Notes: 높이 측정 알고리즘을 간략하게 설명드리면,
k-means 거리 기반 클러스터링으로 각 벽돌의 데이터를 분리하였습니다.
이후 거리정보를 의미하는 z-축 데이터에 이동 평균 필터를 사용해서 노이즈를 감쇄하였습니다.
마지막으로 rms 값을 추출하여 물체의 높이를 추정하였습니다.

## Slide 8
▣ Research Contents
Performance Evaluation Method
Robot system for motion tracking and precise parsing
Performance Evaluation
Reference angle acquisition using a protractor
Relative angle error measurement after catching object
Using plain / long / thick objects
# trial | Relative angle error | Description | 
 | Plain | Long | Thick
1 | -10 | 4 | 21
2 | -11 | 1 | 18
3 | 7 | -4 | 7
4 | -7 | -1 | 18
5 | 8 | 5 | 7
# trial | Relative angle error | Description | 
1 | -10 | 4 | 21
2 | -11 | 1 | 18
3 | 7 | -4 | 7
4 | -7 | -1 | 18
5 | 8 | 5 | 7
Average relative angle error: 8.6 []
Relative angle error measurement
Notes: 평가 데이터셋에 대한 결과로 정확도 94.5% 의 높은 분류결과를 보였습니다.

## Slide 9
Research result
▣ Conclusion
Research Conclusion
Expected Outcome
Robot system for motion tracking and precise parsing development complete
  Average relative angle error: 8.6 [°], goal achieved
Life loss reduction during recovery operations
Work efficiency increase (ex. object conveying speed )
Improvements
A variety of objects recognition using object’s feature
Automatic grip off in various / accurate positions
Angle measurement performance improvement
(ex. Camera calibration)
Wireless camera connection using embedded board
(ex. Jetson Nano)
Notes: 결론 입니다.
연구 목표 3가지 태스크 중 먼저 3차원 치수 측정을 가로세로 오차를 각각 1.92[mm], 1.93[mm]으로 기업에서 제시간 요구조건을 만족하였으나, 높이오차는 2.04[mm]로 요구조건을 만족하지 못하였습니다.
스마트폰 기반 높이 측정에 경우 좌우 평균 높이 오차 1.08 / 1.0[mm]으로 요구조건을 만족하였습니다.
마지막으로 벽돌 표면 결함 분류 성능은 94.5[%]로 요구조건을 만족하였습니다.
위 알고리즘을 통해 발생가능한 기대효과는 품질검사 능력 향상으로 인한 벽돌 품질 개선을 기대할 수 있습니다.
또한 레이저 센서와 같은 고가 센서가 아닌 3d tof 카메라 및 스마트폰을 사용함으로써 센서 가격을 크게 절감할 수 있습니다.
마지막으로 해외로 하드웨어 이전 등의 문제를 스마트폰 기반 알고리즘을 통해 국외로 기술 확대 등을 기대 할 수 있습니다.

## Slide 10
Thank you
Notes: 이상입니다. 감사합니다.